## Slide 1: Embedded Antenna Design Based on Zero and Pole Resonances for Wireless Sensor Modules for Applications in Advanced Greenhouses
Chun-Chih Liu, Shih-An Yang, Tzu-Heng Cheng, and Shih-Yuan Chen
Graduate Institute of Communication Engineering, National Taiwan University, Taipei, Taiwan
Email: shihyuan@ntu.edu.tw
National Taiwan University

## Slide 2: Outline
Introduction
Wireless sensor module
Proposed embedded antenna design
  UHF RFID system & tag antenna
  Tag antenna design based on zero & pole resonances
  Antenna performance
Preliminary measurement results
Conclusions
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 3: Motivation
Climate change & global warming
Extreme weathers: typhoons, hurricanes, tornadoes, floods, droughts, etc
Direct impact: agricultural losses
Advanced greenhouses
  Energy efficient
  Environmental factor monitoring
  Cost effective
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 4: Motivation
Environmental factors to be monitored
  Temperature
  Relative humidity
  Illumination
  CO2 …
Requirements: energy-efficient, low-cost, easy-for-maintenance/deployment infrastructure
Solution: wireless sensor modules with low-power consumption  extended battery life or battery-free
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 5: Motivation
RFID Tags + sensors
Wireless sensor modules with low-power consumption
Passive RFID system
  Low cost
  Wireless
  No power needed in “passive” tags
  EPC standard supporting up to 128-bit data transfer/storage
RFID Reader
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 6: Wireless sensor module
EPC code: serial #, temperature, humidity, … e.g. 0001 0026 0053 0000 0000 0000
I2C interfaces
MCU:
TI MSP430G2553
Temp./Humid. sensor: Silicon Labs Si7021
RFID Tag IC:
Impinj MonzaX-2K Dura
ANT
Rectifier
Energy-harvesting
part still in progress
Gen2 interface
RFID Tag ANT
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw
Coin battery
Proposed design
- Memory bank
- Totally passive

## Slide 7: PCB layout of the module
Overall size: 60  40 mm2
Antenna-excluded size: 50  30 mm2
Double-sided FR4 slab
RFID tag IC: IPJ_MonzaX-2K_Dura
MCU: TI MSP430G2553
Temp./Humd. sensor: Silicon Labs Si7021
Coin battery: CR2032
Temp./Humd. sensor
MCU
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 8: Design requirements of embedded antenna
Complex conjugate match between tag IC & tag antenna to achieve max. power transfer.
Scattered & randomly oriented  omnidirectional
Max. read range r
RFID Tag
Chip
RFID Tag ANT
(18 + j171 )
(18  j171 )

Max. EIRP: 4 W @910 MHz by FCC
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 9: Design method for complex conjugate match
Design goal: small real part & large imaginary part
  Zero resonance: lower the real part of Zant
  Pole resonance: increase the imaginary part of Zant
Ideal resonance arrangement
RFID Tag
Chip
RFID Tag ANT
(18 + j171 )
(18  j171 )
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 10: Embedded antenna design
C1
C2
Antenna structure: /4 monopole loaded with 2 high-Q chip capacitors (C1 & C2)
  Zero resonance: created by /4 monopole & can be controlled by C1, which changes the open-circuit BC.
  Pole resonance: created by inductive part of zero resonance & shunt C2 at higher frequencies.
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 11: Embedded antenna design
Formation of two resonances (Z- & Y-domain)
Im{Zant}
Freq.
Freq.
Zero resonance by ¼ wavelength monopole
Im{Yant}
Shunt C2
+jC2 in Y-domain
Freq.
Im{Yant}
Freq.
Im{Zant}
Pole resonance by zero resonance &
Shunt C2
Zero resonance by ¼ wavelength monopole
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 12: Embedded antenna design
Use C1 & C2 to tailor Zant
C1
C2
18  as C1 = 0.25 pF
+j171  as C2 = 0.5 pF
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 13: Embedded antenna design
Power reflection coefficient when C1 = 0.25 pF & C2 = 0.5 pF
  6 dB bandwidth: 902-922 MHz (20 MHz)
C1
C2
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 14: Embedded antenna design
Surface current distribution
y-directed monopole + loop on x-y plane
loop
monopole
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 15: Embedded antenna design
y-directed monopole + loop on x-y plane  omnidirectional w/o nulls
Simulated peak gain: 0.26 dBi
Calculated max. read range: 8 m with 4-W EIRP @ 910 MHz
x-z plane
y-z plane
x-y plane
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 16: Preliminary measurement results
Fabricated prototype module
Front view
Rear view
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw
LED indicator

## Slide 17: Preliminary measurement results
Update period | 30 sec | 60 sec | 10 min | 30 min
Battery life (with LED) | 9 days (measured) | 0.6 month (19 day) | 0.5 year (185 day) | 1.5 year (535 day)
Battery life (without LED) | 1.3 year (460 days) | 2.4 year | 13.8 year | 21.3 year
Active (2-sec operation): 15 mA (LED) + 300 uA (MCU) Sleep: 0.9 uA (MCU) Battery in use: Maxwell CR2032 (220 mAh) |  |  |  | 
Read range | 3.5 m (measured) / 8 m (calculated)
Stag = 17 dBm, max. EIRP = 36 dBm (4 W), 3-dB polarization mismatch loss (from CP to LP) 0 @ 910 MHz = 333.3 mm | 
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 18: Preliminary measurement results
Reading multiple modules
Serial number
Temperature
Humidity
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 19: Conclusions
An integrated wireless sensor module based on passive RFID technology is proposed for use in advanced greenhouses.
  Low power consumption
  Low cost
  Easy for deployment & maintenance
An embedded antenna design based on zero/pole resonances is proposed.
  Simple, compact, low-profile, highly integrated
  Omnidirectional radiation pattern
  Real- and imaginary-parts of Zant can be independently controlled by C1 & C2 to achieve conjugate match.
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 20: Future outlooks
Include a light sensor to provide illumination information
Optimize the matching condition between our proposed antenna & tag chip for a longer read range
Integrate with energy harvesting submodule to extend the battery life
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw

## Slide 21: Thank you!!!
National Taiwan University
S.-Y. Chen, NTU; shihyuan@ntu.edu.tw
This work is sponsored by Industrial Technology Research Institute (ITRI), Taiwan.