## Slide 1: Antennas for Drone Array
Advisor: Shih-Yuan Chen
Student: Yun-Ting Tsai
Presentation Date: 2021/03/04

## Slide 2: Outline
Slot Antennas
Patch Antennas
Spiral Antennas
Loop Antennas
Monopole Antennas
Conclusions

## Slide 3: Outline
Slot Antennas
Patch Antennas
Spiral Antennas
Loop Antennas
Monopole Antennas
Conclusions

## Slide 4: Slot Antenna (Bidirectional, Single Layer)
A Novel Simple and Compact Microstrip-Fed Circularly Polarized Wide Slot Antenna With Wide Axial Ratio Bandwidth for C-Band Applications, 2016
Gain: 4.5 dBi, Impedance BW (< -10 dB): 90.2%, 3 dB-AR BW: 40%
horizontal strip →
gap → reduce coupling
Sw → improve BW

## Slide 5: Slot Antenna (Endfire, SIW)
Circularly Polarized Substrate-Integrated Waveguide Tapered Slot Antenna for Millimeter-Wave Applications, 2017
Gain: 7.9 dBi, Impedance BW (VSWR < 2): 29.67%, 3 dB-AR BW: 29.67%
slot → , via →
h → amplitude of E
→ phase difference
d → AR performance

## Slide 6: Slot Antenna with Dipole Antenna (Preview)
Novel Circularly Polarized Antennas Combing A Slot With Parasitic Dipoles, 1980
Linear-to-CP convertor

## Slide 7: Slot Antenna with Dipole Antenna (Unidirectional, SIW)
High-Gain Low-Profile Circularly Polarized Slotted SIW Cavity Antenna for MMW Applications, 2017
Gain: 16 dBi, Impedance BW (< -10 dB): 4.6%, AR: almost < 1.6 dB
mode @ 28 GHz
d → resonance f
→ AR & matching

## Slide 8: Outline
Slot Antennas
Patch Antennas
Spiral Antennas
Loop Antennas
Monopole Antennas
Conclusions

## Slide 9: Patch Antenna with Slot (Unidirectional, 2 Layers) (1/2)
Wideband Circularly Polarized Split Patch Antenna Loaded With Suspended Rods, 2021
Gain: > 8 dBic, Impedance BW (< -10 dB): 48.75%, 3 dB-AR BW: 22.58%
→ better excitation & impedance matching
tilted angle → amplitude of E
height → phase difference
→ slot & patch
→ slot & loop

## Slide 10: Patch Antenna with Slot (Unidirectional, 2 Layers) (2/2)
Wideband Circularly Polarized Split Patch Antenna Loaded With Suspended Rods, 2021

## Slide 11: Patch Antenna (Antenna Theory and Design – Stutzman)
Fig.1 Microstrip antennas for generating circular polarization
Fig. 2 stacked-patch microstrip antennas for broadband operation
w/ power divider & phase shifter → BW ↑, size ↑; w/o PD & PS → BW ↓, size ↓
Lossy material → BW ↑, radiation efficiency ↓
Larger → size ↓, e.g. ceramics for GPS patch antenna
End-launch or probe-fed

## Slide 12: Patch Antenna (w/ Power Divider)
Wideband Circularly-Polarized Patch Antenna, 2006
Gain: 9 dBi, Impedance BW (): 79.4%, 3 dB-AR BW: 82%
Symmetry → cancel out probe leakage radiation & probe coupling → suppress cross polarization & widen the impedance and AR BW

## Slide 13: Wideband Phase Shifter
New switched-network phase shifter with broadband characteristics, 2003
(a) is for PS > 9; (b) is for PS < 9
Phase slop is controlled by the value of to
λ/2
λ/8
>180

## Slide 14: Patch Antenna (w/o Power Divider)
Small Circularly Polarized U-Slot Wideband Patch Antenna, 2011
Gain: 4.5 dBi, Impedance BW (< -10 dB): 15.2%, 3 dB-AR BW: 3.2%
U-slot → capacitance → suppress the inductance due to the vertical feeding probe → enable the use of thicker substrates → impedance BW ↑
=10.02

## Slide 15: Outline
Slot Antennas
Patch Antennas
Spiral Antennas
Loop Antennas
Monopole Antennas
Conclusions

## Slide 16: Spiral Antennas (Antenna Theory and Design – Stutzman)
Equiangular Spiral Antennas
Self-complementary
Archimedean Spiral Antennas
Self-complementary & self-scaling
Frequency-independent

## Slide 17: Spiral Antennas (Unidirectional)
Unidirectional beam: 1. λ/4 cavity 2. absorbing material 3. PMC
A low-profile Archimedean spiral antenna using an EBG ground plane, 2004
Height reduction: 69%, Gain: 9 dB, Bandwidth: 71%
Electromagnetic band-gap (EBG) structure with spiral antenna
0.5mm = λ/50
6.25mm = λ/4

## Slide 18: EBG Structure
PBG PMC and PEC ground planes, a case study of dipole antennas, 2000
Reflection phase characterizations of the EBG ground plane for low profile wire antenna applications, 2003
PEC: current cancels its image
PMC: current add up with its image,
but suffer from coupling problems
EBG: similar to PMC with good
matching if resonant f falls into the
band gap of the PBG surface
g → C
vias → L

## Slide 19: Outline
Slot Antennas
Patch Antennas
Spiral Antennas
Loop Antennas
Monopole Antennas
Conclusions

## Slide 20: Loop Antennas (Antenna Theory and Design – Stutzman)
One-wavelength circular/square loop antenna
Gain 3.41 dB / 3.67 dB
With characteristic of a resonant antenna
Radiation pattern

## Slide 21: Outline
Slot Antennas
Patch Antennas
Spiral Antennas
Loop Antennas
Monopole Antennas
Conclusions

## Slide 22: Monopole Antennas (Bidirectional)
Broadband Circularly Polarized Printed Antenna With Branched Microstrip Feed, 2014
Gain: 2.6 dBic, Impedance BW (< -10 dB): 73.0%, 3 dB-AR BW: 46.8%
Branch 1 → monopole
Branch 2 → slot
θ = 0°: odd mode → slot
θ = 90°: even mode → CPW TL → monopole

## Slide 23: Monopole Antennas (Bidirectional)
CPW-Fed Wideband Circularly Polarized Printed Monopole Antenna With Open Loop and Asymmetric Ground Plane, 2014
Gain: 3.5 dBi, Impedance BW (< -10 dB): 96.5%, 3 dB-AR BW: 63.3%
Asymmetric ground plane → CP; rectangular open loop → wide-impedance & AR BW

## Slide 24: Outline
Slot Antennas
Patch Antennas
Spiral Antennas
Loop Antennas
Monopole Antennas
Conclusions

## Slide 25: Conclusions
Gain (dBic) | 4.5 | 7.9 | 4 | 8 | 9 | 4.5 | 9 | 2.6 | 3.5
impedance BW (%) | 90.2 | 29.67 | 1.6 | 48.75 | 79.4 | 15.2 | 71 | 73 | 96.5
AR BW (%) | 40% | 29.67 | < 1.6 dB | 22.58 | 82 | 3.2 | 71 | 46.8 | 63.3
direction | 2 | 1 endfire | 1 | Large back-lobe | 1 | Large back-lobe | 1 | 2 | 2
Gain (dBic) | 4.5 | 7.9 |  | 8 | 9 | 4.5 | 9 | 2.6 | 3.5
impedance BW (%) | 90.2 | 29.67 | 1.6 | 48.75 | 79.4 | 15.2 | 71 | 73 | 96.5
AR BW (%) | 40% | 29.67 | < 1.6 dB | 22.58 | 82 | 3.2 | 71 | 46.8 | 63.3
direction | 2 | 1 endfire | 1 | Large back-lobe | 1 | Large back-lobe | 1 | 2 | 2

## Slide 26: Conclusions
Gain (dBic) | 4.5 | 7.9 | 4 | 8 | 9 | 4.5 | 9 | 2.6 | 3.5
impedance BW (%) | 90.2 | 29.67 | 1.6 | 48.75 | 79.4 | 15.2 | 71 | 73 | 96.5
AR BW (%) | 40% | 29.67 | < 1.6 dB | 22.58 | 82 | 3.2 | 71 | 46.8 | 63.3
direction | 2 | 1 endfire | 1 | Large back-lobe | 1 | Large back-lobe | 1 | 2 | 2
Gain (dBic) | 4.5 | 7.9 |  | 8 | 9 | 4.5 | 9 | 2.6 | 3.5
impedance BW (%) | 90.2 | 29.67 | 1.6 | 48.75 | 79.4 | 15.2 | 71 | 73 | 96.5
AR BW (%) | 40% | 29.67 | < 1.6 dB | 22.58 | 82 | 3.2 | 71 | 46.8 | 63.3
direction | 2 | 1 endfire | 1 | Large back-lobe | 1 | Large back-lobe | 1 | 2 | 2